## Slide 1: Genetic Algorithm Demonstration
Alec, Peyman, Stephen, Tom

## Slide 2: Concept: Genetic Algorithm
Inspired by biological processes
  Reproduction
  Evolution (natural selection)
Optimization of large problems
Solutions’ parameters represented by genes
Three steps:
  Crossover
  Mutation
  Selection
Begin with two potential solutions (initial population)

## Slide 3: Genetic Algorithm: Crossover
Two parents are chosen
Each gene is chosen from one parent
A child is generated with the chosen genes
Repeat for many children to create population

## Slide 4: Genetic Algorithm: Mutation
Don’t want to limit solutions to genes of initial population
Each child has a chance of mutation
One or more genes are changed randomly

## Slide 5: Genetic Algorithm: Selection
Also called a “tournament”
Genes are ranked according to a fitness function
  Generally corresponds with optimality
Best two are picked to generate the next population

## Slide 6: System Goal
Show the process of convergence in the genetic algorithm
Solutions will be represented as images on the LED matrices
  Each red, green, and blue component of each pixel will be a gene
  Optimal solution will be a predefined target image
  Fitness function will be closeness to the target image
Initial population will be four robots
When robots collide, they will perform crossover, mutation, and selection
Each robot will keep one of the best two children
Over time, the robots’ displays will transform from random pixels to the target image

## Slide 7: Implementation Overview
Top-Level System Actor Model Diagram

## Slide 8: LED Matrix
16x32 RGB LED Matrix
A PWM-based algorithm to control RGB LEDs
  brightness controls with 256 levels
  24-bit color
Maximum of 16 rows by 32 columns of 8-bit RGB values
  Restiction on target, parents, and children images

## Slide 9: LED Matrix
If the refresh rate is too low, the LEDs will flash
  FPGA on myRio is utilized to provide a high refresh rate
A 5 MHz clock is used to shift data into the LED Matrix
  Frame rate of 72fps
The FPGA is programmed using VHDL and LabView VIs

## Slide 10: LED Matrix Display VI
Image: A 1-D U8 byte array with the image data. Should be 1536 bytes long.
Image Depth: Color bit depth. Only 24 or 32 are currently supported. Other values = error.
Format of the 1D byte array for 24-bit image depth:
For 32-bit Image Depth, the extra alpha byte gets discarded
Notes: The color bytes are ordered as red, green then blue bytes. The first 3-tuple of color bytes is the color of the top left pixel on the display. The 3-tuples continue along a row, left to right. At the end of a row, the next 3-tuple of color bytes is the color of the leftmost pixel on the next row below the current one. This continues for 512 3-tuple bytes.

## Slide 11: LED Matrix Display VI
Brightness Control
Factor (optional): Gamma correction
  Default = 1 (disables the effect)
  Small values 1.2 - 2.5 (seem to work best)
Brightness (optional):
  Range = 0 (off) to 100 (full brightness)
  Default = 50
  The brighter the LEDs, the more battery power gets consumed ( up to 12.5W)
Experiment with these inputs to see what looks best

## Slide 12: LED Matrix Display VI
Debug / Simulation Support
LED Matrix (optional): Picture output
  Use it on your LabView Front Panel to indicate what the LED Matrix should be displaying.
  Allows use of the VI for simulation when the physical LED Matrix is not available

## Slide 13: LED Matrix Display VI
IMAQ Overlay Blocks for Drawing
NI Vision toolbox
  Cannot use Picture VIs due to a restriction with RT LabView
LED Matrix project has some examples
  Draw Oval in arbitrary location
  Draw text in any position and size
    However, not the prettiest!!!

## Slide 14: Global Vision System (GVS)
Continuously detect marks
Update coordinates
Transmit data to the broker
Stop when “DONE” is received

## Slide 15: Configuration (User Interface)

## Slide 16: GVS Demo

## Slide 17: Collision Detection Model

## Slide 18: Broker
TCP Server
Determines if robots have collided, and which robots were involved in the collision.
Forwards messages between robots.
Communication Broker
Messages from GVS
Messages from Robot
Messages to Robot
Messages to GVS

## Slide 19: Broker State Machine
GVS Message Formats
RX
W:<Color>:<X-coor>,<Y-coor>
TX
THANKS
DONE
Robot Message Formats
              RX
H:
C:
G:<Parent Genes>
T:<2nd best child Genes>
D:<Result Image>
TX
S:<Target Image>
O:
R:
G:<Parent Genes>
T:<2nd best child Genes>
D:<Result image>

## Slide 20: Robot
Reached target image

## Slide 21: Genetic Algorithm: Example